## Slide 1: A rotational shearing interferometer to sense across-the-spider phase discontinuity at ELT
Lorenzo Busoni, Simone Esposito, Giulia Carlà, Guido Agapito, Cedric Plantet, Marco Bonaglia
Osservatorio Astrofisico di Arcetri - INAF

## Slide 2: Why Yet Another Petalometer
ELT/GMT have segmented pupil with thick spider shadows or gaps
WFSs can’t «easily» reconstruct the WF under the gaps
Acting on DM control (slaving, POLC, …) may reduce unwanted petal pistons
But is it what we want? Real phase jumps do exist across the spider – pistoning petals is not evil
What we lack is the capacity to measure the wavefront jumps across the spider.

## Slide 3: Wavefront jumps across the spider
The Nuke wavefront
H. Bonnet, Petal day – Mar 22
Not only atmospheric turbulence, but Low Wind Effect, M1 footprint, …

## Slide 4: WFS concept
A shearing interferometer with rotational symmetry to overlap sectors of pupil across the spider
A pupil image
The pupil image rotated by
1-2
2-3
2-2
3-4
Recombine and
make interference
1
2
3
1
2
3
Overlap this with this and make interference here
The Ciao Ciao WFS
Notes: Il WFS concept is simple: a rotational shearing interferometer that allows to interfere two pupil sectors separated by spider
Beam split, pupil rotator, recombine
Phase shifting o anche no.
The intensity in the overlapped sectors is function of dphi = dp + dres
Very similar to https://www.sait.it/node/470

## Slide 5: Other interferometric petalometers
Ron Holzloehner - WFS workshop Firenze https://www.sait.it/node/470

## Slide 6: Phase difference reconstruction
Assuming
The phase difference across the spider can be retrieved from the interferogram
It requires monochromatic beams – we assume narrowband at 2200nm
Phase-shifting techniques can be used to extend the capture range to . More exposures - slower – needs piston mirror
Multi-lambda is possible to extend beyond - even slower
Notes: Non misura phase, but «phase jumps». The range –pi, pi is in the jump, not in the phase itself. +0.6 lambda and -0.6 lambda makes a jump of 1.2 that doesn’t work

## Slide 7: Impact of residual turbulence
Splitting in
static phase jump and
turbulence evolving during T
where assuming and skewness
➜ the spatial decorrelation of the turbulence biases the measurement of with a factor < 1
Q: Can be estimated from the non-overlapping sectors (for large T)? Or calibrated?

## Slide 8: Optical concept
BS1
BS2
Pupil rotator
Phase n𝜆/2 shifter
(optional)
From AO
Recombination in pupil conjugated plane
Highly inefficient conceptual idea
A 6x lenslet to collect all the sector flux onto 6 APD

## Slide 9: Optical simulations
Based on poppy
Optical model consists of a stack of pupil layers
  Residual turbulence from MORFEO simulations
  Low Order Zernike
  ELT Pupil Aperture
  Petaled M4
  Global Piston for phase shifting
  Rotator
2 identical models are instantiated with different rotation. Output wavefronts are recombined

## Slide 10: No turbulence case
0
100
-200
300
-400
500
500
-100
300
700
-500
-900
Measured jumps
Estimated petals
that is correct up to a global piston of -500nm
-100
300
-500
700
-900
500
Notes: Mettere freccine per capire come si fa

## Slide 11: Too large phase steps
0
200
-400
600
-800
1000
1000
-200
600
-800
-1000
400
Petals are within (-λ/2 , λ/2 )
But jumps exceed (-λ/2 , λ/2 )
-200
600
-1000
1400
-1800
1000
Expected jumps
Measured jumps
Estimated petals
Wrong by 2𝜋 ambiguity

## Slide 12: Rejection of low order aberrations
Residual tilt doesn’t cancel out: it is seen as a rotated tilt of smaller amplitude:
where is the rotation matrix of the pupil image by
Focus Z4

## Slide 13: Residual turbulence of MORFEO
MCAO residual turbulence simulated with PASSATA
r0=0.128m, 6 LGS + 3 NGS, M4+1pfDM, POLC-MMSE
Residuals along 45 arcsec off-axis, 2s at 500fps
Cumulative average
Notes: Residuo atmosferico dopo la correzione MCAO nella direzione off axis di un sensore LO (quanto off axis?)
Come è fatto il controllo, in termini del pistone atmosferico, base modale etc?
Ce la stiamo giocando con POLC/MMSE? Nel senso che abbiamo una turbolenza esattamente come quella messa nell’apriori e quindi ci funziona tutto?

## Slide 14
Long exposure (2s) residual phase map.
spatial variance = 220nm rms
We can compute the phase jumps across the spiders
Jumps = [-179, -96, -50, 153, 7, 70] nm

## Slide 15: Interferograms of the residual turbulence of MORFEO
Cumulative average

## Slide 16: Jumps estimation on residual turbulence
Exposure time=2s
Overlapping 𝛼=10°
«Real» phase jumps = [-179, -96, -50, 153, 7, 70] nm
Estimated jumps = [-168, -107, -64, 161, 21, 63] nm
Stdev jumps error = 11nm - Not bad!
Reconstructed petals = [-33, 74, 138, -24, -45, -108] nm

## Slide 17: Mimicking petals correction
Petals estimated by petalometer
Petal corrected – 185nm rms
Before correction – 221nm rms

## Slide 18: Spectral properties of the residual turbulence of MORFEO
Residual turbulence with has a power spectrum
Structure function
reaches plateau of about 350nm already at
Notes: Residuo atmosferico dopo la correzione MCAO nella direzione off axis di un sensore LO (quanto off axis?)
Come è fatto il controllo, in termini del pistone atmosferico, base modale etc?
Ce la stiamo giocando con POLC/MMSE? Nel senso che abbiamo una turbolenza esattamente come quella messa nell’apriori e quindi ci funziona tutto?

## Slide 19: Trying to improve SNR
The residual turbulence is too large to measure the phase difference with good SNR
We are interested in a pseudo-static and the temporal power spectrum of the residual is decreasing fast, so…
we can apply homodyne detection (like in push-pull IM, lock-in amplifier, …)

## Slide 20: Homodyne detection
Original signal overwhelmend by noise
Demodulation: multiply by and average
Modulated signal: spectrum shifted at

## Slide 21: How to modulate interferograms?
Non modulated signal
Small modulation of
must be small λ/100 to preserve PSF
The modulation above is not discriminating among signal and noise: the restored signal is still affected by large noise

## Slide 22: Conclusions
Yet another petalometer to sense phase jumps across the spider
Interferometer based on overlapping of 2 rotated pupil images
Decent jumps retrieval with 2s exposure time also with MORFEO’s good seeing residuals
Attempt to improve SNR with homodyne detection is left as an exercise to the reader

## Slide 24
Average std of short exposure residual is 376nm

## Slide 25: Phase Shifting to extend the range
Classic 𝜋/2 phase shift to extend capture range to (-𝜋, 𝜋)
with

## Slide 26
Phase jumps estimated by the petalometer for 5, 10 ,20° of rotation angle
In [81]: np.round(ej5[::2])
Out[81]: <Quantity [-168., -122., -46., 171., 15., 51.] nm>
In [82]: np.round(ej10[::2])
Out[82]: <Quantity [-168., -107., -64., 161., 21., 63.] nm>
In [83]: np.round(ej20[::2])
Out[83]: <Quantity [-66., -50., -11., 102., 12., 0.] nm>
Phase jump on phase map using sectors of X° around the spider
In [73]: np.round(jj5[0::3] - jj5[1::3])
Out[73]: array([-179., -96., -50., 153., 7., 70.])
In [74]: np.round(jj10[0::3] - jj10[1::3])
Out[74]: array([-169., -90., -57., 198., 20., 41.])
In [75]: np.round(jj20[0::3] - jj20[1::3])
Out[75]: array([-145., -112., -63., 245., 17., -12.])

## Slide 27
With an exposure time of 2s, the petal error is

## Slide 28: Axisymmetric aberrations cancel out completely
Focus Z4
Astigmatism Z5