## Slide 1: HASO LIFT Imagine optic
Guillaume Dovillaire
wfs2022 Porto
October 20th 2022

## Slide 2
Wavefront sensors and adaptive optics for
optical metrology, lasers and microscopy
Optical metrology
& adaptive optics
for X-EUV

## Slide 3
Standard Shack-Hartmann
Association of a microlenses array and a detector
Spot positions are proportional to the local wavefront slopes

## Slide 4
Shack-Hartmann hartmanngram
Square microlenses
focale length f, Size D
On the detector : Sinc² function

## Slide 5
Concept : phase retrieval at microlens scale
Standard
Shack Hartmann
Centroid
PSF shape analysis
Phase retrieval
Enhanced spatial
Resolution with LIFT
1 single microlens
Incident
wavefront

## Slide 6
Spot shape vs local aberrations
Without aberration
With astigmatism :10 nm PV
Difference
For example

## Slide 7
Spot differences for the 9 first Legendre
Tilt X and tilt Y influences
Focus, 45° astigmatism and 0° astigmatism influences
3rd order influences
The solution : change the shape of the microlenses to create an offset in the transmitted aberration
for instance, if the microlens itself contains pure astigmatism, a positive and a negative focus will have a different influence
Problem : the focus signature is the same for a positive or a negative value

## Slide 8
To learn more about LIFT
Sensing more modes with fewer sub-apertures: the LIFTed Shack–Hartmann wavefront sensor
Serge Meimon and al ONERA, May 15, 2014 / Vol. 39, No. 10 / OPTICS LETTERS
Experimental validation of LIFT for estimation of low-order modes in low-flux wavefront sensing
C. Plantet, S.Meimon, J.-M. Conan and T. Fusco, 15 July 2013 | Vol. 21, No. 14, OSA
Small-phase solution to the phase-retrieval problem
R. Gonsalves, Opt. Lett., Vol. 26, No 10, pp. 684-685 (2001)
LIFT is « Linearized Focal plane Technique »

## Slide 9
Optical setup
SLM
Source @520 nm
x4 Zoom pathway
HASO4 BROADBAND
HASO LIFT 272
Normal mode
or Lift mode

## Slide 10
Transfer function : Wavefront amplitude/spatial frequency
SLM
Source
Phase patterns sent to SLM
HASO LIFT 272
Normal mode
or Lift mode
HASO4 BROADBAND

## Slide 11
Transfer function : examples for 0.125 cycles/µlens
550 nm
550 nm
550 nm
Zoom x4 : reference
32 µlenses per cycle
Standard HASO
8 µlenses per cycle
Enhanced resolution
but still
8 µlenses per cycle
HASO4 BROADBAND
HASO LIFT 272 wo LIFT
HASO LIFT 272

## Slide 12
Transfer function : examples for 0.5 cycles/µlens
100 nm
Zoom x4 : reference
8 µlenses per cycle
2 µlenses per cycle
No centroid displacement
The oscilaltion in the wavefront is not measured
100 nm
2 µlenses per cycle
No centroid displacement but PSF shape modification
Enhanced resolution
HASO4 BROADBAND
HASO LIFT 272 wo LIFT
HASO LIFT 272

## Slide 13
HASO and HASO LIFT Transfer function
Chart: 
| 0.125 | 0.14285714285714285 | 0.16666666666666666 | 0.2 | 0.25 | 0.33333333333333331 | 0.4 | 0.5 | 0.66666666666666663 | 1
HASO | 1 | 1 | 1 | 0.96 | 0.8 | 0.5 | 0.33333 | 0.125 | 0.0083333 | 0
HASO LIFT | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.96667 | 0.8
0.2
0.3
0.5
Twice Nyquist frequency
for HASO
Resolution improvement : x4
Twice Nyquist frequency
for HASO LIFT

## Slide 14
HASO LIFT 272
Phase hologram sent to SLM
Black is 0
White is 2
Phase reconstruction with standard
Shack-Hartmann algorithm
Phase reconstruction with
LIFT algorithm

## Slide 15
Phase hologram sent to SLM
standard
Shack-Hartmann
LIFT algorithm
Spatial Frequency
HASO LIFT 272

## Slide 16
HASO LIFT 272
Phase hologram sent to SLM
Phase reconstruction with standard
Shack-Hartmann algorithm
Phase reconstruction with
LIFT algorithm

## Slide 17
Implementation in Waview4

## Slide 18
Our HASO LIFT
400-800nm
10.2 x 13.8 mm²
l/100 RMS absolute accuracy
400-800nm
5.2 x 7 mm²
l/100 RMS absolute accuracy
1050-1700nm
7.4 x 9.3 mm²
l/100 RMS absolute accuracy

## Slide 19
Some other newly released HASO
7.12 x 5.33 mm²
14 microlenses on 3.6mm diameter
Optimized for 637nm
Accuracy (systematic errors) : 5 nm RMS
Repeatability at saturation : 5 nm RMS
10nm RMS of repeatability at 1000ph/s in the pupil
USB3.0
The ultra-low light
7.12 x 5.33 mm²
14x14 microlenses
0.9 to 1.7µm
Accuracy (systematic errors) : 12 nm RMS
Repeatability at max speed : 30 nm RMS
1.7kHz
USB3.0
The SWIR FAST

## Slide 20
Thank you
or
??

## Slide 21
BACK-UP SLIDES

## Slide 22
Chart: Shack-Hartmann ITF
| 0.5 | 0.45600000000000002 | 0.38 | 0.32571428571428573 | 0.28499999999999998 | 0.25333333333333335 | 0.22800000000000001 | 0.20727272727272728 | 0.19 | 0.17538461538461539 | 0.16285714285714287 | 0.14249999999999999 | 0.12666666666666668 | 0.114 | 0.10363636363636364 | 0.1
in WFE | 0.010053 | 0.17582 | 0.31932 | 0.47326 | 0.57176 | 0.65654 | 0.73332 | 0.75732 | 0.79056 | 0.82032 | 0.83866 | 0.87274 | 0.90626 | 0.92536 | 0.93666 | 0.93428
in slopes | 0.47512 | 0.56097 | 0.6686 | 0.74109 | 0.79867 | 0.84457 | 0.86576 | 0.88654 | 0.90591 | 0.92089 | 0.94194 | 0.93865 | 0.9643 | 0.97802 | 0.9813 | 0.97297
Shack-Hartmann transfer function

## Slide 24
Conclusions
HASO LIFT = The best of Shack-Hartmann technology + High sampling density
High accuracy : l/100 RMS
Huge dynamic range
Insensitive to vibrations
And now high spatial resolution
HASO LIFT 272 : 200x272 phase points
HASO LIFT 680 : 504x680 phase points
HASO LIFT opens the door to new applications and, together with R-Flex LA, allows for multispectral interferometry applications.

## Slide 25
HASO LIFT 272
HASO4 BROADBAND
HASO LIFT 272 and HASO4 BROADBAND

## Slide 26
Phase hologram sent to SLM
Phase reconstruction with standard
Shack-Hartmann algorithm
Phase reconstruction with
LIFT algorithm
HASO LIFT 680

## Slide 27
HASO LIFT 680
Phase hologram sent to SLM
Phase reconstruction with standard
Shack-Hartmann algorithm
Phase reconstruction with
LIFT algorithm

## Slide 28
Example : small diameter phase gaussian defect (FWHM = 2 µlens)
Zoom x4 : reference
FWHM = 8 µlens
Standard HASO
FWHM = 2 µlens
Enhanced resolution
FWHM = 2 µlens
Enhanced resolution = refrence resolution
PV = 260 nm
PV = 150 nm
PV = 280 nm
Detectable but wrong amplitude

## Slide 29
Example : small diameter phase gaussian defect (FWHM = 1 µlens)
Zoom x4 : reference
FWHM = 4 µlens
Standard HASO
FWHM = 1 µlens
Enhanced resolution
FWHM = 1 µlens
Enhanced resolution = refrence resolution
PV = 44 nm
PV = 17 nm
PV = 36 nm
Hardly detectable, wrong amplitude

## Slide 30
HASO LIFT 272
Phase hologram sent to SLM
Phase reconstruction with standard
Shack-Hartmann algorithm
Phase reconstruction with
LIFT algorithm

## Slide 31
HASO LIFT 680
Phase hologram sent to SLM
Phase reconstruction with standard
Shack-Hartmann algorithm
Phase reconstruction with
LIFT algorithm

## Slide 32
Spot differences for the 9 first Legendre @ 650 nm
Tilt X and tilt Y influences
Focus, 45° astigmatism and 0° astigmatism influences
3rd order influences

## Slide 33
HASO LIFT 272
Phase hologram sent to SLM
Phase reconstruction with standard
Shack-Hartmann algorithm
Phase reconstruction with
LIFT algorithm