## Slide 1: Strategy for sensing petal mode in presence of AO residual turbulence
Authors :
Nicolas Levraud, Vincent Chambouleyron, Mahawa Cisse, Anne Laure Cheffot, Jean François Sauvage, Benoit Neichel , Thierry Fusco, Cedric Plantet, Guido Agapito, Enrico Pinna, Simone Esposito

## Slide 2: Adaptive Optics :
3 Main components
Wavefront sensor
Control system (real time computer)
Deformable mirror
Classical OA simulation
Limited by :
- number of DM actuator
- Control loop speed
- Wavefront sensor reconstruction
Ajouter le passage ‘on a besoin de l’OA pour controler l’atmosphère plus le télescope est grand’
Credit : Romain Fétick  PAPYRUS bench presentation Friday at 11:00

## Slide 3: Adaptive Optics for giant telescope
New challenge for wavefront reconstruction and control: phase gap  differential piston between pupil fragment  PSF limited by
Pupil ELT
Spider = 50cm
Pupil GMT
Spider >40cm
Credit : Sebastian Haffert
Credit : Charlotte Bond
Pupil VLT spider=5cm
Pupil Keck spider=2,5cm
Télescope : jusqu’à la classe des 10m le télecope n’était (presque) pas un problème, sur la clase des 30 m ça en devient un majeur
Vise a atteindre le diffraction limit sensing dans le visible
10m telescope (almost) not a problem for AO
Credit : Rebecca Jensen-Clem
30m class telescopes becomes a major problem
Our aim : reaching diffraction limit with a visible wavefront sensor
Credit : Jean François Sauvage
Notes: A gauche VLT et kck, puis bloque ELT et bloque GMT avec les même infos pupille, puis résidu d’OA puis petaling

## Slide 4: Modelisation of the problem : the toymodel
Only 2 fragment, 1 petal mode
Test setting : ELT size spider (50cm) on a VLT-class telescope(10m)
Spider represents 5% of pupil diameter
Petal mode
AO end to end loop with fullpupil :
AO end to end loop with spider in the pupil :
Residuals are dominated by fitting error
Conditions :
20*20 DM
D=10m
r0=25cm @550nm
Wind speed=5m/s
No detector noise,
No sensor noise,
Sensing at λ = 550nm
F=500Hz
Spider size= 50cm
5λ/D pyramid for control
Phasescreens at iteration 132
Residuals are fitting error + petal mode
Toymodel pupil

## Slide 5: Pyramid wavefront sensor
Pupil plane
focal plane
Detector in pupil plane
Petal mode 1*P
Flux
Ref : R. Ragazzoni 1996 ‘Pupil plane wavefront sensing with an oscillating prism’

## Slide 6: Pyramid response to petal mode
Modulation = 7λ/D
Modulation = 5λ/D
Modulation = 3λ/D
Modulation = 1λ/D
Modulation = 0λ/D
S as a function of modulation radius
measure petal = unmodulated pyramid
depending on modulation and spider size
Ref : V.Chambouleyron 2022 ‘Optimizing Fourier-Filtering WFS to reach sensitivity close to the fundamental limit’
VLT
ELT
HARMONI

## Slide 7: Pyramid control without modulation
strong turbulence  need modulation  not sensitive to piston
Need two sensors,
1 for atmosphere
1 Petalometer
Petal when modulating better than no modulation
Conditions :
20*20 DM
D=10m
r0 =15cm @550nm
Wind speed=5m/s
No detector noise,
No sensor noise,
Sensing at λ = 550nm
F=500Hz
Spider size= 50cm

## Slide 8: 2 Path wavefront sensor
Telescope with spider
Modulated pyr
Non modulated pyr
Petalometer
Atmosphere control
Controls petal only
Petal free DM modes
Equivalent to woofer-twitter AO system but for the sensing
Can the pyramid in second path measure petal ?

## Slide 9: Petal estimation
I(ϕ)/F
I(0)/F
Intensity
Intensity
Intensity
()
econstructed petal
Goal : test VS p in presence of residuals
p = - 0.1 rad
= - 0.1 rad
[,
: interaction matrix
: Reconstruction or control matrix
Introduced
Reconstructed

## Slide 10: Petal reconstruction : with no atmosphere
Estimate for each
Linearity curve in absence of noise or atmosphere
As expected, = sin(p)
True for modulated and non modulated pyramid
Pas justifié le p^= sin(p)

## Slide 11: Petal reconstruction with 20x20 first stage residuals
Residuals phase screen used :
Conditions :
20*20 DM
D=10m
r0=15cm @550nm
Wind speed=5m/s
No detector noise,
No sensor noise,
Sensing at λ = 550nm
F=500Hz
Spider size= 50cm
Residual piston substracted from phasescreen
Petal reconstruction is biased in presence of residuals and spider
fullpupil
5% spider
Bias no modulation = 0.45 rad
Bias modulation = 0.42 rad
Pourquoi gain optiques si différents ?
Bias > min of reconstruction  cannot reconstruct 0

## Slide 12: Petal reconstruction with variable residuals
100 consecutive residual phasescreens
Highly depedant on phase residuals
Fast evolving
Reconstruction made for 10 independant residuals
Bias not repeatable

## Slide 13: Petal reconstruction with variable residuals
Bias is residual dependant  can’t be controlled
Bias no modulation = 0.18 rad
Bias modulation = 0.20 rad
Residuals scaled by 0.1
Petal bias for diferent scaling of residualphase
Residuals scaled by 0.5
Bias no modulation = 0.62 rad
Bias modulation = 0.26 rad
Notes: Changer orga ici

## Slide 14: Reduce impact of residuals
Reduce the phase to be sensed  go to longer wavelength
Reduce impact of residuals  spatial filter in the focal plane
Petal dominates
Residual dominates
Pupil plane
focal plane with spatial filter
Detector in pupil plane
5 λ/D seems best compromise here
Spatial Filter Radius

## Slide 15: After spatial filtering linearity plots
Spatially filtered reconstruction is the same with or without spider Bias greatly reduced
fullpupil
5% spider
Notes: Bigger fontsize !

## Slide 16: Conclusion
2 sensor-system necessary to measure petal
Residuals bias the petal measurement
Spatial filter reduces this bias

## Slide 17: Perspectives
Understanding origin of the bias  what creates bias in the residuals ?
Closed loop simulation  loss of light ? Size of spatial filter ? Best sensor ?
Simulation of ELT case
Spatial filter interest for other Fourrier Filtering WFS
Test on PAPYRUS ?
Thank you for listening !

## Slide 18: Annex : Spatial filter effect on pyramid signal
I(0)
1 λ/D
3 λ/D
5 λ/D
10 λ/D
15 λ/D
5 λ/D seems best compromise here
Petal phase

## Slide 19: Annex Origin of the bias
Phase a la limite VS biais ?
Phase =0 sur 20 cm autour du spider pour voir si ça enlève le biais ?
Look at what signal is used for petal reconstruction
of petal
Signal of petal reconstruction very close to spider
 Residual next to spider causing bias ?
Blunt test : zero phase next to spider
As if Spider = 70cm
Reduced bias !
As if Spider = 90cm
No effect on bias !
Origin of bias not understood
Comes from phase residuals
Phase screen

## Slide 20: Annex : Improving sensitivity to petal
No Spider
Spider
No modulation
No modulation
3 λ/D modulation
3 λ/D modulation
I ref
I piston
Toymodel pupil

## Slide 21: II Improving sensitivity to Petal : Loss with spider when modulating
classic 4 sided
pyramid
Asymetric pyramid
Toymodel pupil (D=10m)
Sensitivity
Sensitivity
ELT
ELT