## Slide 1: A new low order Wavefront Sensor and its first experimental results.
Alessandro Terreri
Collaborators:
  Dr. Fernando Pedichini
  Dr. Markus Kasper
  Dr. B.Engler
  Dr. T. Heritier
  Prof. Dario Del Moro
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
1 /25
Notes: Userei lo stesso font per tutte le scritte mi piace molto quello del titolo

## Slide 2
NN
PCA
Short Summary
In Laboratory
On Sky
Use of extrafocal images
STARTING FROM THIS..
WE WANT TO OBTAIN THIS…
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
2 /25
Notes: EVENTUALMENTE togliere l animazione col blocco dell AO che entra

## Slide 3
Simulated using the ESO library PO4AO by T.C.Heritier 2020
AO residual and NCPA
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
3 /25
Notes: EVENTUALMENTE togliere l animazione col blocco dell AO che entra

## Slide 4
TYPICAL BEST SCENARIO @LBT
Strehl vs NCPA
Chart: Effect of NCPA with 80 nm AO residual
| 0 | 10 | 20 | 30 | 40 | 50
2200 nm | 0.94914 | 0.94836 | 0.94604 | 0.94219 | 0.93683 | 0.92998
656 nm | 0.55592 | 0.55085 | 0.53589 | 0.51187 | 0.48003 | 0.44199
||-------No AO residual-----||-----With AO residual-----||
NCPA is critical in the visible
Example:
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
4 /25
Notes: Sintetizzare

## Slide 5
FOCAL
PLANE
EXTRAFOCAL
PLANE
PUPIL
PLANE
LENS
Optical Propagation Simulations
PUPIL
PLANE
CAN’T BE MEASURED….
…We measure the
POINT SPREAD FUNCTION
STOP
Equivalent system with just 3 features needed:
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
5 /25

## Slide 6
Amplitude
Phase
Phase: Zernike Polynomials or phase screen
NCPA is encoded in the first Zernikes
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
6 /25
Notes: Sintentizzare

## Slide 7
Even
Even
Even
Odd
Odd
PROPAGATION
Can we use focal plane images to recognize aberrations?
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
7 /25
Notes: Va aggiunto il valore della NCPA e impaginare meglio

## Slide 8
Focal plane
Pupil
plane
Odd Radial order
DEGENERATION
Even radial order
NO DEGENERATION
+50nm
+50nm
-50nm
-50nm
-50nm
Spherical
Astigmatism
Astigmatism
+50nm
+50nm
-50nm
-50nm
+50nm
-50nm
Coma Y
Coma X
Trefoil 45°
Extra-focal plane
+50nm
Degeneration or non degeneration? That’s the problem
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
8 /25

## Slide 9
DEFOCUS = 10 mm
Simulations of 10000 Extrafocal plane images starting from the injection of different combination of 21 Zernike with UNIFORMLY RANDOM DISTRIBUTED
Propagation
Each one is a linear combination:
Simulated dataset (10 000 images)
PUPIL PLANEPHASE
EXTRA-FOCAL PLANE INTENSITY
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
9 /25

## Slide 10
Returns basis of eigenimages that comes from the diagonalization of the covariance matrix for the defocused images dataset
Thousands of pixels are now substituted with few hundreds coefficients
Images can be projected on this basis
Principal Component Analysis (PCA)
Every image of the dataset can be expressed as a linear combination of
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
10 /25
Notes: Accorciare se possibile le frasi scritte

## Slide 11
HIDDEN LAYER
OUTPUT LAYER
INPUT LAYER
PCA
COEFFICIENTS
ZERNIKE COEFFICIENTS
……
……
Intensity
Phase
Neural Network
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
11 /25

## Slide 12
NN usage on 1 image
SIMULATED
EXPERIMENTAL
……
…
OR
INPUT
PROJECTION
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
12 /25

## Slide 13
We need merit factors to evaluate the efficiency of the NN reconstruction:
Results come from simulated images:
Train-set 10 000 images
Test-set 100 images (different conditions)
Training, Testing and merit figures
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
13 /25

## Slide 14
Median=3.7 nm
Mean=4.1 nm
TESTSET: distribution
of prediction error for 100 images
Example
on 1 image
Single image: predicted vs. injected
Ideal case: ONLY NCPA
nm
SIMULATIONS
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
14 /25

## Slide 15
Mean=0.25
Mean=0.95
Simulation of correction: from 123 to 21 nm WFE
SIMULATIONS
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
15 /25

## Slide 16
Effects in the focal plane
Example:
1 image of the TEST-SET
Linear scale
Log scale
After NN Prediction/Correction
Diffraction Limit
SIMULATIONS
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
16 /25
Notes: Toglierei quell fattore moltiplicativo della scala log

## Slide 17
CAMERA SHIFT
I used the Spatial Light Modulator (SLM) to inject:
Aberrations
AO residual
(still working)
Laboratory setup:
Experimental work to control bench and train the new NN
EXPERIMENTAL: GHOST bench
EXPERIMENTAL
Move manually the camera out of focus and test the NN
Use of iterative process
of correction
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
17 /25

## Slide 18
Results on the GHOST bench with Iterative process
I chose a set of coefficients randomly in the range [-50,+50] nm for the 21 Zernike polynomials and then:
NCPA is injected through the SLM
We perform a measurement with NN
We can inject back in the SLM the values measured by NN
EXPERIMENTAL
# Iteration step
WFE [nm] RMS
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
18 /25
WE PERFORM BETTER AND FASTER THAN HUMAN

## Slide 19
AO Residual + random NCPA
AO residual + Fixed NCPA
Iterative correction using the AO loop
With AO closed loop residual turbulence
Three possible approaches to mitigate NCPA using NN:
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
19 /25

## Slide 20
Median=4.9 nm
Mean=5.4 nm
TESTSET: prediction error distribution for 100 images
Single image: predicted vs. injected
Example
on 1 image
1. AO Residual + random NCPA
nm
SIMULATIONS
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
20 /25

## Slide 21
AO limits for WFE and SR
1. AO Residual + random NCPA
From 133 nm to 58 nm WFE RMS
SIMULATIONS
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
21 /25

## Slide 22
Take home message:
We can infer the NCPA as the average of the predicted aberrations
From initial value of to (AO residual limit 50 nm)
2. AO residual + Fixed NCPA
#100 fast exposures with fixed NCPA…. From 139 to 57 nm WFE RMS
SIMULATIONS
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
22 /25

## Slide 23
3. Iterative correction using the AO loop
From 184 nm to 50.5 nm WFE RMS
(AO residual limit 50 nm)
SIMULATIONS
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
23 /25

## Slide 24
Experimental Results
ON-GOING ???
let’s see
EXPERIMENTAL
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
24 /25

## Slide 25
CONCLUSIONS
This new proposed algorithm based on NN and PCA coefficients WORKS….. correctly identify relations between defocused images and wavefront phase at the pupil plane.
It is possible to use it to mitigate completely all the static/quasi static aberrations in CONTROLLED conditions (such as Laboratory condition, the instrument has a calibration/reference source, characterizing optical elements or the entire optical path)
Compared to MANUAL trial-and-error approach:
  FASTER …< 1 minute  NN prediction on one image < 1 ms
  BETTER… 7% more in terms of maximum in the peak compared to values found MANUALLY by an EXPERT in optics.
It is possible to use this algorithm to minimize NCPA using the NN on:
  A single image
  Series of images in frozen flow condition with the same NCPA (FAST IMAGING APPROACH)
  Single or series of images but with the real time correction thanks to some Active Optical Elements (such as DM,DL or SLM …. typically on AO system)
IDEAL CONDITION
TURBULENCE CONDITION
Wavefront Sensing in the VLT/ELT era VII - Porto
Terreri Alessandro
25 /25
Notes: I risultati li metterei in una tabella e prometterei meno per il prossimo anno da decider insieme cosa promettere

## Slide 26
Thank you for the attention
ORIGINAL IDEA:
Terreri et al 2022, A&A, Neural networks and PCA coefficients to identify and correct aberrations in adaptive optics, DOI:10.1051/0004-6361/202142881
EXPERIMENTAL RESULTS:
Terreri et al. 2022, SPIE Proceedings, Experimental verification of NN and PCA for NCPA mitigation
stands for «Neural Network 2 Optimize NCPA»
But if you switch apex with pedic it probably brought to your mind brute formula for Nitrous Oxide (NOS) used in cars to boost the output of the engine for a limited duration… BECAUSE WE WANT TO REMOVE THE NCPA FASTLY
Or the anesthetic used in surgery… BECAUSE WE WANT THE ABERRATIONS TO GO TO SLEEP
😜

## Slide 27
Published papers
A.Terreri et al.2022, A&A,Neural Networks and PCA coefficients to identify and correct aberrations in Adaptive Optics DOI: 10.1051/0004-6361/202142881
A.Terreri et al.2022, SPIE, Experimental verification of NN and PCA for NCPA mitigation DOI:10.1117/12.2629249
Papers as co-author
G.Viavattene et al. 2022, SPIE, DOI: 10.1117/12.2629400 , ELVIS: the exoplanets at LBT with a visible IFS for SHARK-VIS
F. Pedichini et al.2022, SPIE, SHARK-VIS ready for the stars: instrument description and final laboratory performance test, DOI: 10.1117/12.2629244
R.Briguglio et al 2022, SPIE, Demonstrating the sub-nanometer sensitivity of a pyramid WaveFrontSensor for active space telescopes, DOI: 10.1117/12.2599825
G.Viavattene et al. 2022, IBIS-TRE-01: Conceptual design of the IBIS 2.0 polarimentric unit, DOI:10.20371/INAF/TechRep/136
R.Briguglio et al.2022, SPIE, Laboratory characterization of a large format, contactless active mirror with intrinsic rejection of vibrations, DOI:10.1117/12.2628730
Talks
Workshop «Wavefront sensing in the VLT/ELT era»,Firenze, 2019
Workshop «Network of Young Researcher in Instrumentation for Astronomy», 2021
ESA-ESO SCIOPS, 2022, DOI: 10.5281/zenodo.6568531, Neural Networks and PCA coefficients to identify and correct aberrations in Adaptive Optics
Workshop Ottica Adattiva Italiana «ADONI», Teramo, 2022
Conference «Machine Learning at Galileo Galilei Institute», Firenze, 2022
AO4ELT, Porto, 2022 (SCHEDULED)
INAF, «Deep Learning @INAF», Pula (Sardegna), 16-19 September 2019
International School of Space Science, L’Aquila, «Dynamical system and machine learning approaches to Sun-Earth relations», 1-5 February, 2021
Space Science Institute, «Applications of Statistical Methods and Machine Learning in the Space Sciences», May 17-21,2021
CFAO, University of California (Santa Cruz), «Summer school on Adaptive Optics», 16-20 August 2021
3 months Internship at the European Southern Observatory (ESO) in Garching Bei Munchen, Germany, 7 April – 8 July 2022
Poster
A.Terreri et al.2022, Poster, DOI:10.1117/12.2629249, Experimental verification of NN and PCA for NCPA mitigation
SUMMARY
of
PhD activities
Schools
Internship

## Slide 28
NN_0
NO Turbolenza
FLUSSO 1e6
FLUSSO 1e5
FLUSSO 1e4
RMS= 1.2 nm
RMS= 0.8 nm
RMS= 0.8 nm
FLUSSO 1e3
RMS= 13 nm

## Slide 29
NN_0.5
FLUSSO 1e3
FLUSSO 1e4
Turbolenza 50nm RMS
FLUSSO 1e5
FLUSSO 1e6
RMS= 3.5 nm
RMS= 18.9 nm
RMS= 3.8 nm
RMS= 3.7 nm

## Slide 30
NN_1
FLUSSO 1e3
FLUSSO 1e4
Turbolenza 100 nm RMS
FLUSSO 1e5
FLUSSO 1e6
RMS= 7.5 nm
RMS= 26 nm
RMS= 7.1 nm
RMS= 6.9 nm

## Slide 31
31
2020 Workshop for PhD Program in Astronomy, Astrophysics and Space Science
Terreri Alessandro
HIGH CONTRAST
Distinguish star in multiple system
Solar Granulation studies
Identification of exoplanets (2)
Better photometry estimation (AGN)
4m solar granulation simulation
without correction
with correction (2000modes)
Fast imaging and CADI

## Slide 32
ZERNIKE
Both encode the same out of focus image
PCA
Two sides of the same coin
Machine Learning at Galileo Galilei Institute
Terreri Alessandro
32 /38

## Slide 33
TURBULENCE frozen flow by FAST IMAGING
AO residual
FAST IMAGING allows freezing of turbulence
Fixed NCPA
AO residual+ Fixed NCPA
AVERAGING
AVERAGING
AASS PhD WORKSHOP 2022
Terreri Alessandro
33 /34
Notes: Animazioni confondono e fanno perdere tempo mi dispiace ma queste immagini non sono chiare

## Slide 34
New results after improving image centering
# Iteration step
WFE [nm]
STILL WORKING TO IMPROVE RECENTERING
EVEN IF IT IS NOT NECESSARY
100
FLAT SLM
EXPERIMENTAL

## Slide 35
SR =
When is the image good?
Speckles
&
AO residual
Aberrated image
Control
radius
NCPA EFFECT consists of static/quasi-static or slowly evolving intensity structures like these.
AASS PhD WORKSHOP 2022
Terreri Alessandro
35 /34
Notes: Mettere profilo radiale

## Slide 36
Phase screen [4096x4096] pixel
LBT Pupil Ø 8200mm
[440x440]pixel
Sampling: 18mm
Kolmogorov spectrum
high pass filtered to match AO residual during calibration @LBT
BEWARE !
From now on, simulations will contain high order aberrations (from the phase screen) unknown to the neural network during the training…
AO residual model
AASS PhD WORKSHOP 2022
Terreri Alessandro
36 /34

## Slide 37
Good fit of AO residual vs experimental data!
λ = 630nm
PSF RADIAL PROFILE
mas
SIMULATED
EXPERIMENTAL
AASS PhD WORKSHOP 2022
Terreri Alessandro
37 /34
Notes: Non si usa una freccia ma si scrive Texp.=….