## Slide 1: First on-sky demonstration of the C-BLUE One camera and the HEART RTC platform on REVOLT
Oct 21, 2022
Jean-Pierre Véran
National Research Council Canada
Herzberg Astronomy & Astrophysics, Victoria, BC
Presentation to the AO WFS Workshop in Porto (Oct 19-21, 2022)

## Slide 2
REVOLT is an SCAO system for the HAA 1.2m McKellar telescope
Operates at the Coudé focus, just like VOLT in 2008
REVOLT is intended as a test bench to test new AO technologies developed by or critical to HAA on sky.
Complements HAA AO Lab
Two successful runs so far
  Aug 2022 (one night)
  Sep 2022 (two nights)
REVOLT
Research, Experiment, and Validation of Adaptive Optics with a Legacy Telescope
Site characteristics:
  Seeing = 1.5” (best) / 2.1” (mean) / 2.5” (90%tile) / 4.2” (worst)

## Slide 3
First Light C-Blue One camera
  NFIRAOS LGS WFS camera)
HEART RTC Platform
  To be used in NFIRAOS, GNAO, GPI2, GIRMOS and possibly MORFEO and ANDES
Fiber-fed photonic spectral correlation sensor
  Remote gas detection and identification technique
  Developed by NRC-AEP and NRC-HAA, based on correlation spectroscopy with a piezoelectric tunable fiber-optic Fabry-Perot filter
Open-loop AO (GIRMOS), PWFS control, Advanced control algorithms
20x20 Low-voltage DM prototype (NRC-NanoTechnology)
512x512 Saphira NIR APD camera
AO technologies to be tested
✓
✓

## Slide 4
REVOLT with Alpao DM + C-Blue-One

## Slide 5
REVOLT in the Coudé room

## Slide 6
First results
Alpha Persei (Mirfak) Aug 12
Uncorrected
AO corrected
“H-Band” (1600nm ± 50nm)
Frame rate = 1 kHz
Airy: FWHM = 0.28”

## Slide 7
Rejection transfer functions
Uncorrected
AO corrected
Using open-loop and closed loop data with r0=5cm disturbance
Very clean fit
Interface to C-Blue One is CoaXPress 2.0
  No pixel streaming – frame must be complete to be available
ROI 352x352 pixels read from camera @ 1 kHz
  Integration time = 891 us

## Slide 8
MARS !
Uncorrected
AO corrected
Mars (10.29” diameter – Sep 9, 2:45am PDT)
  Sub-aperture FOV: 15.3”
50 images, 0.75s per image H-band

## Slide 9
MARS !
Uncorrected
AO corrected

## Slide 10
REVOLT GUI
Uncorrected
AO corrected

## Slide 11: The REVOLT Team
AO Group
  Kate Jackson
  Dave Andersen
  Tarun Kumar (PhD student)
  Daniel Muhwezi (co-op student)
  Jean-Pierre Véran
Optics Group
  Olivier Lardière
Software Group
  Jennifer Dunn
  Darryl Gamroth
  Dan Kerley
  Lianne Mueller
  Malcolm Smith
  Ed Chapin
  Jonathan Stocks
Telescope Group
  Dmitry Monin
  David Bohlender
1.2m telescope control room
Special thanks to Uriel Conod (foreground) for his help during the Aug 2022 run.