## Slide 1: FEWHA for the MORFEO instrument Balancing between reconstruction quality and run-time
Wavefront Sensing in the VLT/ELT Era VII Porto, Portugal October 21st, 2022
Bernadett Stadler, Daniel Jodlbauer, Andreas Obereder, Stefan Raffetseder, Ronny Ramlau bernadett.stadler@indmath.uni-linz.ac.at

## Slide 2: Multi Conjugate Adaptive Optics Relay (MORFEO)
Adaptive Optics module for ESO‘s Extremely Large Telescope (ELT)
Aim: Providing good wavefront correction over a large field of view
Requires tomographic estimation of 3D atmospheric wavefront disturbance
2
Credit: ESO

## Slide 3: AO control
3
WFS measurements sx and sy
Incoming screen DM shape Residual
Fitting / Projection step
a = F ϕ
6 turbulent layers ϕ
Atmospheric tomography
MVM method: a = Rs R precomputed in soft-real time
s = A ϕ
- 2 step approach

## Slide 4: Finite Element Wavelet Hybrid Algorithm (FEWHA) Atmospheric tomography
Reconstruct turbulent layers from sensor measurements
s = A ϕ
Regularization: Bayesian framework + maximum a-posteriori estimate
(A*Cη-1A + Cϕ-1)ϕ = A*Cη-1s
Challenges: demanding operations to be solved in real-time (500 Hz)
4
Sparse discretization + iterative solver
Notes: C_eta: paper from Clementine in 2010:
sigma^2=1/nphotons
tuning alpha_eta
Full width at half maximum
Elongation vector: depending on height, laser launch position, midpoints of subaperture
Tip tilt directly removed in equation s=A*phi  for each LGS directions C_eta=(I-T)*C_eta*(I-T), where T is a orthonormal projection into the tip and tilt
measurement space.

## Slide 5: Finite Element Wavelet Hybrid Algorithm (FEWHA) Wavelets for atmospheric tomography
Idea: Using a wavelet basis for representing the turbulence layers
5
M. Yudytskiy and T. Helin and R. Ramlau. Finite element-wavelet hybrid algorithm for atmospheric tomography. J. Opt. Soc. Am. 2014.
Why wavelets?
    Approximative properties (less coefficients)
    Fast decay in the frequency domain  efficient turbulence statistics representation
    diagonal Cϕ-1 in wavelet basis
    Discrete Wavelet Transfrom is Ο(n)
Wavelets of choice: Daubechies 3
Notes: For sufficiently large N Daubechies wavelet 2 regular. However N=3 not enough but good in numerical simulations.
Diagonal C_phi: widely used penalty term from Ellerbroek + wavelet family that is 2-regular (2 vanishing moments and are 2 times continuously differentiable) -> Bernstein Jackson inequality applicable -> diagonal approximation

## Slide 6: Finite Element Wavelet Hybrid Algorithm (FEWHA) Atmospheric tomography
Dual domain discretization: wavelet basis + bilinear basis
Iterative approach: Preconditioned Conjugate Gradient Method (PCG
6
+ Fast, because of sparse matrices + On the fly parameter updates (no soft real-time precomputation)
- More complex structure of the algorithm  harder to parallelize and pipeline

## Slide 7: Finite Element Wavelet Hybrid Algorithm (FEWHA) Mirror fitting for MCAO systems
7
Layers at altitudes of DMs: No mirror fitting necessary
… projection through layer ℓ into direction θ … projection through DM into direction θ
More layers than DMs: Additional problem to be solved
Notes: the mirror shapes are determined directly from the shapes of the turbulence layers
minimize the cost functional ||P*phi – P_quer*a|| we choose discrete directions of interest theta over FOV. For a bilinear representation of the mirrors and the wavelet representation of the layers, this leads to this equation here
For piecewise bilinear basis functions have sparse matrices -> choose again an iterative solver

## Slide 8: Real-time performance Reducing the PCG iterations for tomography and mirror fitting
Warm restart: Reusing the solution from previous time step as intial guess for the PCG method of the next time step
8
B. Stadler and R. Ramlau. An augmented wavelet reconstructor for atmospheric tomography. ETNA. 2021.
M. Yudytskiy and T. Helin and R. Ramlau. A frequency dependent preconditioned wavelet method for atmospheric tomography. AO4ELT3 Conference. 2013.
Preconditioning: (Modified) Jacobi preconditioner
Augmented Krylov Subspace Method: Reusing search directions of PCG from previous time step to speed up the PCG of the next time step

## Slide 9: Numerical simulations in OCTOPUS
9
System parameters | 
Telescope | 37 m diameter
Obstruction | 11 %
Fried parameter | 12.9 cm
Turbulence layer | 35 layer, von Kármán, L0=25 m
Na-layer height | 90 km
Na-layer FWHM | 11.4 km
Delay | 2 frames
Evaluation wavelength | K band
Simulation duration | 1 s
Wavefront Senors |  | 
 | LGS - WFS | NGS - WFS
Type | SH - WFS | SH - WFS
Number | 6 | 3
Geometry | 74 x 74 subap. | 2 x 2 subap.
Subap. size | 10 x 10 pixel | 6 x 6 pixel
GS asterism | 45 arcsec | 55 arcsec
Wavelength | 589 nm | 1650 nm
Flux | 500 photons/subap./frame | 500 photons/subap./frame
Detector RON | 3.0e−/pixel/frame | 3.0e−/pixel/frame
DMs (equidistant actuator spacing) |  |  | 
 | DM1 | DM2 | DM3
Actuators | 75 x 75 | 47 x 47 | 37 x 37
Altitude | 0 km | 4 km | 12.7 km
Spacing | 0.5 m | 1 m | 1 m
Notes: Noise in simulation??

## Slide 10: Parallel implementation on CPU
Global parallelization over number of layers or WFSs  block diagonal structure of matrices
Local parallelization inside the blocks
10
Parallel, matrix-free implementation in C++
FEWHA called as external library in OCTOPUS
Run-time measurements only for FEWHA (no data movement)

## Slide 11: Test settings
MORFEO with 2 post focal DMs
  Reconstructing 3 layers directly at the altitudes of the DMs (no mirror fitting)
  Reconstructing 9 layers with a mirror fitting step
MORFEO with 1 post focal DM
  Reconstructing 2 layers directly at the altitudes of the DMs (no mirror fitting)
  Reconstructing 9 layers with a mirror fitting step
11

## Slide 12
12
Center Strehl Ratio: 55.22 %
Average Strehl Ratio: 36.07 %
Number of PCG iterations: [2, -]
Run-time: 1.5 ms
Strehl ratio in 5x5 directions over FoV 35 layer atmosphere, 3 DMs
3 rec. layer
Center Strehl Ratio: 58.89 %
Average Strehl Ratio: 41.57 %
Number of PCG iterations: [4, 2]
Run-time: 8.1 ms
9 rec. layer

## Slide 13
13
Center Strehl Ratio: 51.21 %
Average Strehl Ratio: 30.95 %
Number of PCG iterations: [2, -]
Run-time: 1.4 ms
Strehl ratio in 5x5 directions over FoV 35 layer atmosphere, 2 DMs
2 rec. layer
Center Strehl Ratio: 55.30 %
Average Strehl Ratio: 34.52 %
Number of PCG iterations: [4, 2]
Run-time: 7.9 ms
9 rec. layer

## Slide 14: Summary
Wavelet based, iterative real-time reconstructor FEWHA
Fast + good reconstruction quality
  Sparse discretization with wavelet and bilinear basis
  Reduced number of PCG iterations
  Matrix-free, parallel implementation in C++
No soft-real time precomputation of the inverse  on the fly parameter updates
14

## Slide 15: Ongoing and future work
Comparison with the Fractal Iterative Method (FrIM) in OCTOPUS
Interface to PASSATA simulator  compare with well-tuned MVM
15
Microgate’s Real Time Reconstructor
Testing at bench and on-sky
Implementation on FPGAs (together with Microgate)

## Slide 16: Thank you!
This research has received funding by the Austrian Research Promotion Agency (FFG) FO999888133 (Industrial methods for Adaptive Optics control systems).
Notes: FEWHA for pyramid: linearized model because FEWHA is linear reconstructor – linearization of the roof sensor

## Slide 17: Parameter tuning via simulation
17
 | 3 DMs 3 layers | 3 DMs 9 layers | 2 DMs 2 layers | 2 DMs 9 layers | 
Regularization | 8.0 | 8.0 | 8.0 | 16.0 | large influence on rec. quality changes with photons and r0
Spot elongation | 0.2 | 0.2 | 0.2 | 0.2 | medium influence on rec. quality changes with photons and r0
Loop gain | 0.4 | 0.4 | 0.4 | 0.4 | small influence on rec. quality
Number of iterations [tomography, fitting] | [2,-] | [4,2] | [2,-] | [4,2] | trade-off between quality and speed