## Slide 1: Seeing estimation from Adaptive Optics Telemetry
Nuno Morujão (MEng Physics Student)
Collaborators: Paulo Garcia, Carlos Correia, Paulo Andrade, Johann Kolb, Julien Woillez

## Slide 2: Motivation
Site evaluation and characterization;
Non-consensual values for the turbulence parameters;
Optimization of the adaptive optics systems and fringe trackers;
Understand if and how climate change is affecting turbulence parameters (r0 and L0);
Use AO telemetry data for the estimation of turbulence parameters;
Operational adoption of the algorithm;
R. Wesson/ESO

## Slide 3: NAOMI - the new AO system of the VLTI
Challenging scenario:
  VLTI/ATs – 4 NAOMIs;
  SH-WFS (4x4, visible);
  Diameter: 1.8 m
Advantages
Spatial resolution – 4 AT’s at Paranal;
Temporal coverage – near-continuous estimation of the seeing;
Source matching – Direct correspondence to the observing telescope;
ESO/G.Hüdepohl
Woillez + 2019

## Slide 4: Methods: background
Andrade+ 2019 (“Estimation of atmospheric turbulence parameters from Shack–Hartmann wavefront sensor measurements”, MNRAS, 483, 1192):
Fit theoretical variances;
Include cross coupling effects (function of r0 + L0) in model;
Iteratively fit r0, L0 and noise;
Novel adaptations:
Conversion of the algorithm into a ;
Estimation of the uncertainty of the fit
through a Monte Carlo approach;

## Slide 5: Methods: pipeline flow
Telemetry data
Pseudo-open slopes
Temporal variances
Iterative
estimation algorithm
Turbulence parameters
(r0, L0)
Negative
feedback
control loop

## Slide 6: Methods: iterative algorithm
Initial measured variances are introduced in the model fit;
Result in an initial set of turbulence parameters (r0, L0, noise);
The estimated turbulence parameters are used to calculate the
cross-talk = f(r0,L0);
Cross-talk and noise are removed from the variances;
Fit of corrected variances (r0, L0, noise);

## Slide 7: Shack Hartmann sensor
M – # of lenslets in the sensor
N – # of contemplated modes
– fitted modes
– remaining modes
Measurement is done from derivatives of the used modal basis (Zernike polynomials)
s – measured slopes vector
G – derivative matrix
b – reconstructed Zernike coefficients

## Slide 8: Error Sources
Present problems in NAOMI:
Aliasing – Finite frequency of the sensor;
Measurement noise – Read-out noise, photon noise, ...
Cross-talk - Non-orthogonality of G columns;
Woillez + 2019
Features | Value
SH-WFS lenslet configuration | 4x4
# of active lenslets | 12
Diameter of telescope | 1.8 m
Central obstruction | 7.7 %
Fitted Zernike modes | 12

## Slide 9: Cross-talk
Zernike polynomials don’t possess orthogonal derivatives
Columns of G are non-orthogonal
- Inverse matrix;
- Cross-talk matrix;
Result in:
Andrade + 2019
No C correction

## Slide 10: Cross-talk & aliasing mixing
Modes above the fifth radial order display aliasing.
Only one non aliased radial order.
We still see improvements to our correction if we include aliased modes.

## Slide 11: Results
Total data sample:
Date window - (11/2018 - 03/2020)
Total data size - 8170 data measurements
Loop frequency - 500 Hz
Minimum time horizon - 20 seconds
Internal consistency in the estimation algorithm was found.
Median uncertainty of 1.2%.
A single well-behaved minima was found in the map for the seeing.

## Slide 12: Seeing comparison: telemetry vs DIMM
Seeing estimates are available from the DIMM;
Excellent agreement between DIMM and AO telemetry based seeing;
% level differences;
Causes:
Different instrument locations;
Different dome turbulence in DIMM;
Noise estimation from fit;

## Slide 13: Seeing comparison: wind-speed
As the wind-speed increases the differences between DIMM and AO telemetry based seeing data estimates also increases.
The difference is caused by:
Vibrations in the defocus mode – Especially affected by wind-shake;

## Slide 14: Outer scale estimation
Can’t be estimated with NAOMI telemetry data consistently;
Small telescope diameter leads to a minimum detectable frequency larger than the frequency associated with the outer scale (20 meters);
It’s translated in the map as a weak (absent) minima;

## Slide 15: Consistency of estimates
The seeing is consistent across the ATs.

## Slide 16: Status and Future Goals
Algorithm is operational;
Improves estimation to sub % error wrt DIMM;
Agreement across ATs;
Deployable to track seeing on 20 sec time scales;
Explain the remaining differences between NAOMI and DIMM;
Automatic removal of abnormal modes;
Improve noise estimation algorithm;
Improve estimation with data fusion of the four telescopes and fringe-tracking data;

## Slide 17: Thank You !