## Slide 1: MKID-based pyramid wavefront sensor, wavelength sensitivity detector for tracking optical gain
Aurélie Magniez, Lisa Bardou, Charlotte Bond, Tim Morris, Kieran O’Brien
Notes: PhD student at durham
Work on using MKID (just presented), as Pyr. WFS detector and see what we can do with it

## Slide 2: Energy sensitive detector for PWFS?
Influence of λ?
Optical Gain : change with r0 which change with λ
Corrected PSF diameter
Pupil dispersion
Atmospheric dispersion
Uses of using λ-signals?
Optical gain monitoring
Chromatic super resolution
Pupil dispersion : widening the useable bandpass
Without energy sensitive detector?
Multiple WFS/Camera
Complicates optics
Only for few wavelengths
What we have done?
PWFS module simulate energy sensitive detector
Impact of the pupil dispersion (SPIE 2022)
Initial parametric model to track optical gain (now)

## Slide 3: Microwave kinetic inductance detector (MKID) for XAO
Credit : Meeker et al. 2015
Mazin et al. 2019
PIXEL
ARRAY
Credit :Mazin et al. 2019
OUTPUT
AO Requirements
Every pixel is read out at 1MHz independently in a continuous data stream
  Match / exceed existing WFS detectors
Number of pixels
  MEC array : 20k
Detection bandwidth demonstrated 400 nm to 15001 nm but no technical limits to go beyond
Additional features
Energy sensitivity
  Resolving power : R = 30
Photon arrival time (to a microsecond)
1 De Visser et al., 2021, DOI : 10.1103/PhysRevApplied.16.034051

## Slide 4: How to simulate an MKID-based PWFS?
Wavelength sensitivity
Run simultaneously at different wavelength
  Fixed modulation radius
  Same atmosphere
Sampling according to the shortest wavelength
Photon stream
Sample / simulate the atmosphere at higher temporal resolution than the AO system update rate
Modulation path can vary between frames
Work in progress
Soapy
AO end-to-end simulation
PWFS module update
Available on Github : https://github.com/AOtools/soapy
Soapy’s
GUI
Increase computation complexity

## Slide 5: Motivation
Methods using energy sensitivity
Chromatic super resolution
Resolve pupil dispersion (SPIE)
Optical gain measurement
Questions:
What is the behaviour of the optical gain according to key parameters?
Can we use the λ-measures to track this behaviour?
Name | Value
Pixels across pupil | 40
Telescope Diameter | 8 m
Frame latency | 1
Frame rate | 1kHz
Controlled modes | 500
SPHERE like parameters

## Slide 6: Measurement of optical gains (OG)
End-to-end simulation optical gain measure
Closed loop simulation
Decomposition of the PWFS input phase screen in KL modes
Plot amplitude measured vs true amplitude for each mode
Linear fitting : OG = slope coefficient
Work in progress: Compare with convolutional model

## Slide 7: Optical gain behaviour : Photon noise and r0
Loop at 500 nm
Optical gains increase with number of photons and r0
r0 = 12cm @ 500nm
r0 = 20cm @ 500nm

## Slide 8: Optical gain behaviour : Modulation radius
Modulation radius change the dip in the mode space
Dip changed at different wavelength : dip influenced by λ/modulation radius
Loop at 500nm
Loop at 900nm

## Slide 9: Optical gain behaviour : Wavelength
Change in the dip : influenced by the ratio wavelength / modulation radius
r0 influences the ratio between OG at different
r0 = 12cm @ 500nm
r0 = 20cm @ 500nm

## Slide 10: Optical gain : modelisation?
Modulation radius
Wavelength influence
Photon noise
r0
KNOWN
UNKNOWN

## Slide 11: We don’t have the OG…
… we have the KL decomposition of the wavefront at different λ
OG modelisation?
We need r0 !
Ratio of the OG at different λ different for different r0
r0
Photon noise
λ
Mod. radius
Can the ratio of the PWFS measurements at different λ be linked to OG ratios?
Can we measure r0 from these ratios to generate optical gain curves?

## Slide 12: Simulation configuration
PWFS λ1
Reconstructor λ1
PWFS λ2
PWFS λ3
Reconstructor λ2
Reconstructor λ3
KL mode coefficients λ1
DM
(KL modes)
KL mode coefficients λ3
KL mode coefficients λ2
AO closed loop
Data available
on sky
Atm phase screen
Work in progress:
Optimisation of the loop using ALL the measures

## Slide 13: MKID output : let’s use it!
Loop closed at 500 nm
Pseudo open loop output (DM command + measure of the residuals by the PWFS) of the different PWFS
  For different wavelength
  At different r0
Work in progress:
Close the loop at higher wavelength
Understand more theoretically this behaviour.
Ratios

## Slide 14: Parametric model : retrieve r0
Separation of the curves per r0
Fit of the curves
Determination of a
+ C4
r0 | Measured r0
0.12 | 0.1187
0.15 | 0.1507
0.2 | 0.2018
0.25 | 0.2486
🥳

## Slide 15: Parametric model : retrieve r0
Separation of the curves per r0
Fit of the curves
Determination of a
Works with fewer photons
+ C4
r0 | Measured r0 | Measured r0 (less photons)
0.12 | 0.1187 | 0.1194
0.15 | 0.1507 | 0.1498
0.2 | 0.2018 | 0.2017
0.25 | 0.2486 | 0.2491
r0 | Measured r0
0.12 | 0.1187
0.15 | 0.1507
0.2 | 0.2018
0.25 | 0.2486
🥳
Work in progress:
Change of the constants with the noise and other parameters: TBD
Sensitivity of the model?

## Slide 16: Conclusion
End to end simulation shows parameters influence on OG
Unknown in our system : r0
MKID : measure at different wavelength
Parametric model : estimation of r0
r0
Photon noise
λ
Mod. radius
Optical gain
MKID-based PWFS
Influenced
by
Modal decomposition at different λ
Parametric
model
Gives
r0
Retrieve
Next:
Sensitivity of constants in the parametric model
Optical gain model
Optical gain compensation
Go to the lab!!

## Slide 17: Thank you
aurelie.magniez@durham.ac.uk
Soapy :
https://github.com/AOtools/soapy