## Slide 1: Two-wavelength focal-plane piston sensing: first experimental results with LIFT
Cédric Plantet, A.- L. Cheffot, S. Lombardi, M. Bonaglia, A. Puglisi, C. Selmi, L. Busoni, E. Pinna, S. Esposito
WFS workshop, October 2022

## Slide 2: Context
Design of Giant Magellan Telescope’s Natural Guide star Wavefront Sensor
GMT = segmented telescope
Among the degrees of freedom, there is the differential piston between segments

## Slide 3: Wavefront sensor vs differential piston
200 nm
200 nm + λ
Difference between these wavefront steps?
1)
2)
What difference? Both are 200 nm!
Sensor @ λ
Step? What step?
Credit: Thorlabs

## Slide 4: AO vs Science path
H band PSF
PSF @ 750 nm
+750 nm
-750 nm
Input wavefront
AO path: “All fine!”
Science path:
“What the…!”
 Need for another sensor and/or wavelength to identify ejections
GMT’s Single-Conjugated Adaptive Optics done with pyramid sensor @ λc = 750 nm
Single sensor @ λ
 segments converge at a multiple of λ

## Slide 5: LIFT: principle
LInearized Focal-plane Technique
Phase diversity with single image
Relies on diffractive image formation model
Original goal: sense tip/tilt and focus on a faint NGS (with astigmatism phase offset)
Model-based  can be extended to piston estimation

## Slide 6: Double-wavelength LIFT: principle
Need for a large capture range > λ  minimum 2 sensing wavelengths
Astigmatism offset  focus offset (easier implementation)
Simple algorithm to match estimation couple – piston amplitude
1150 nm
1250 nm

## Slide 7: Double-wavelength LIFT: which wavelengths?
Capture range  longer wavelengths, close to each other
AO correction  longer wavelengths
Good SNR  wavelengths as far as possible from a multiple of main AO’s wavelength
Capture range limited by synthetic wavelength (beating frequency):

## Slide 8: Example in simulations
AO residual series for mag R = 12 and r0 = 12.8 cm
Telescope regularly “scrambled” with differential pistons up to 2.5 um
LIFT in double J band
R = 12, r0 = 12.8 cm
J1
J2
J1
J2

## Slide 9: LIFT test bench
LIFT camera
with filter wheel
Fiber output + parabolic mirror for collimation
Diff. piston generator
(flat mirror cut in half)
Encoder on Z translation
pist = 0
pist = λ/5
pist = λ/2

## Slide 10: Results
Successful estimation in double H band (1500 + 1600 nm) on 12 um range
RMS w.r.t. fit: 16 nm
Data
Rec
1500 nm
1600 nm
Fit: y = 0.97 x

## Slide 11: Limits
Diff. tip/tilt  bias on the estimation
  Ok if bias << λ/2 on main channel
Model-based  sensitive to model errors
  Pupil apodization
  Uncalibrated NCPAs
  …
Tip 50” on one segment (no piston)
Diff. piston -360 nm

## Slide 12: Conclusion & perspectives
First experimental demonstration of differential piston sensing with LIFT!
Next:
  Setup improvement
  Tests in presence of simulated residuals
  On sky?

## Slide 13
AO 4 ELT - 7th Edition 25 to 30 th June 2023 Palais des Papes, Avignon, France
Web site : ao4elt7.sciencesconf.org
More information: Thierry.Fusco@onera.fr, Benoit.Neichel@lam.fr

## Slide 14: Thank you for your attention!
Questions?